## Slide 1
Q-Hack India 2026
Team Name:
[ to fill ]
Team Lead Name:
[ to fill ]
Track:
[ to fill ]
Problem Statement title:
Q-SHIELD: continuous device trust with post-quantum-signed evidence
Authentication answers who are you once. Q-SHIELD keeps asking can you still be trusted.
Notes: Team name, lead name and track are left as [ to fill ]: they were not supplied and must not be invented. Problem statement title: Q-SHIELD, continuous device trust with post-quantum-signed evidence.

## Slide 2
Q-Hack India 2026
Problem
A device that authenticated can still be compromised, and nothing asks again
t0
authenticate
trusted
enclosure
opened
still trusted
configuration
drift
still trusted
camera covered
or turned
still trusted
forged or
replayed
still trusted
trust should change here, but authentication never asks again
Context
AIoT devices at the edge (sensors, cameras, controllers) authenticate once with a provisioned key, then run unattended.
The gap
Authentication proves who is talking, not whether the device is still in a trustworthy state.
The quantum angle
Evidence signed today with RSA or ECDSA could be forged once large quantum computers exist.
Notes: Every compromise on the timeline happens after a successful login, so the device keeps its access. The quantum angle is the motivation for post-quantum signatures on the evidence path (next slides).

## Slide 3
Q-Hack India 2026
Why It Matters
Who is exposed, and what each attack looks like with and without Q-SHIELD
Who faces it
Research labs and server rooms
Smart buildings and campuses
Critical-infrastructure sites
Any fleet of unattended AIoT devices
Why now
NIST published FIPS 203 (ML-KEM) and FIPS 204 (ML-DSA) in August 2024: evidence signed today should already be post-quantum.
Threat
Authentication alone
With Q-SHIELD
Forged or replayed message
rejected, then forgotten
bounded pressure (≤ 25 points); 3 replays in 10 min hold the score at 65
Enclosure opened
nothing to see
physical factor CRITICAL; score held at 55
Camera covered, frozen or turned
nothing to see
signed camera-health report; visual factor HIGH
Tamper + camera or visual evidence
nothing to see
confirmed incident: score 30, quarantine
Quantum adversary recording traffic
classical signatures forgeable later
ML-DSA-65 signs the evidence; ML-KEM-768 keys the session
No single signal quarantines a device. Two independent authenticated signals within 60 s do.
Notes: Threat model from docs/architecture/trust-engine.md (sections 4.5, 5, 9). FIPS 203 and FIPS 204 were published by NIST in August 2024.

## Slide 4
Q-Hack India 2026
Proposed Solution
A closed loop around every device: trust is computed continuously, enforced, and earned back
OBSERVE
device and camera
VERIFY
HMAC, ML-DSA-65
SCORE
trust engine
ENFORCE
quarantine at gateway
RECOVER
verified, earned
PROVE
signed evidence chain
continuous
trust
What we are building
Continuous six-factor trust engine
every score change lists the reasons that sum to it
The camera as part of the security boundary
covered, frozen or turned is signed evidence
Quarantine enforced at the gateway
the device's normal channel is refused (403)
Verified, earned recovery
health checks first, then trust rebuilt from fresh evidence
Post-quantum evidence
ML-DSA-65 signatures, ML-KEM-768 sessions
Notes: The novelty is the loop, not one algorithm. Pink marks the two steps one-time authentication lacks: enforcement and earned recovery.

## Slide 5
Q-Hack India 2026
Why Quantum?
Quantum computing is the threat model; post-quantum cryptography is how Q-SHIELD answers it
Quantum capability
What it breaks
Q-SHIELD's answer
Shor's algorithm
RSA, ECDSA, ECDH: today's signatures and key exchange
ML-DSA-65 (FIPS 204) signs observations and evidence; ML-KEM-768 (FIPS 203) agrees session keys
Grover's algorithm
at most a square-root speed-up on brute-force key search
AES-256-GCM, SHA-256 and 256-bit HMAC keys keep a large security margin
Harvest now, forge later
long-lived evidence recorded today
every evidence-chain entry is signed with ML-DSA-65
The cost of going post-quantum (measured, laptop CPU)
signature size
ML-DSA-65 3309 B vs ECDSA P-256 64 B
sign / verify
9.42 ms / 0.188 ms (median)
ML-KEM-768 encapsulate
0.069 ms (median)
full session handshake
10.0 ms (median)
Honest scope: Q-SHIELD runs no quantum circuits and no quantum hardware. Its quantum-relevant part is post-quantum cryptography on the evidence path; the ESP32 device path is HMAC-SHA256, not a post-quantum signature.
Notes: Shor's algorithm (1994) breaks factoring and discrete-log based schemes (RSA, ECDSA, ECDH). Grover's algorithm (1996) gives at most a quadratic speed-up for search, so 256-bit symmetric keys and SHA-256 keep a large margin. Numbers: docs/results/pqc-benchmark.json (i7-13700HX, pqcrypto 1.0.0, Python bindings). ECDSA P-256 raw signature: 64 bytes.

## Slide 6
Q-Hack India 2026
Implementation and Architecture
1 of 3: how the parts work together, quantum-safe and classical
ESP32 / device agent
simulated today
Identity
HMAC-SHA256 + counter
Vision service
camera + YOLO11n
PQC session
ML-KEM-768, AES-256-GCM
Signed observations
ML-DSA-65
Gateway
authenticate
enforce
record
Trust engine
six factors
caps, decay
state machine
Decision
TRUSTED or SUSPICIOUS
normal access
≥ 50
QUARANTINE
normal channel 403
< 50
Recovery
operator-started, verified
VERIFIED → TRUSTED
trust re-earned
Digital twin
expected vs self-reported state
Evidence chain
every decision SHA-256 linked, ML-DSA-65 signed
Quantum-safe: ML-KEM-768, ML-DSA-65 (pqcrypto)
Classical: FastAPI, trust engine, SQLite, YOLO11n, OpenCV, dashboard
Device path: HMAC-SHA256 with a counter (not post-quantum)
Notes: Pink outline = post-quantum components. The device lane authenticates with HMAC-SHA256; the vision lane uses an ML-KEM-768 session carrying ML-DSA-65 signed observations. The trust engine decides; the gateway enforces. Sources: backend/api/app.py, backend/trust/, backend/security/session.py.

## Slide 7
Q-Hack India 2026
Implementation and Architecture
2 of 3: the post-quantum evidence path
ML-KEM-768 session (vision service ↔ gateway)
1
Gateway key pair, provisioned once
client pins the public key, 1184 B
2
Client encapsulates
→ shared secret + ciphertext, 1088 B
3
Init signed with ML-DSA-65; gateway verifies, decapsulates
→ shared secret, 32 B
4
HKDF-SHA256 on both sides
salt = both nonces, info = transcript
5
Key confirmation
a wrong pinned key: nothing is sent
6
AES-256-GCM session
per-direction keys, 64-bit counters, AAD
median, laptop: encaps 0.069 ms, decaps 0.091 ms, handshake 10.0 ms
Composed by us from standard primitives: not TLS, not externally reviewed.
ML-DSA-65 signed observation
Observation
device, object, zone, confidence, time
Canonical encoding
length-prefixed fields, never JSON
ML-DSA-65 sign
context qshield/signed-observation/v1
Signature, 3309 B
bound to signer, source and allowed devices
Gateway verify
active signer, in scope, ±300 s, not seen before
ACCEPT 200
→ trust engine
REJECT
401 forged or stale, 409 replay
Evidence chain: every decision SHA-256 linked and ML-DSA-65 signed; 26 entries VERIFIED in the live demo.
Notes: Handshake: backend/security/session.py. Signed observations: backend/protocol/signed_observation.py. Evidence chain: backend/evidence/chain.py (context qshield/evidence/v1); not anchored externally, so cutting the tail needs an outside copy of the head. Numbers: docs/results/pqc-benchmark.json.

## Slide 8
Q-Hack India 2026
Implementation and Architecture
3 of 3: the trust engine and the camera as part of the security boundary
Six-factor trust
Identity / crypto
25%
Physical
20%
Configuration integrity
15%
Sensor consistency
15%
Visual
15%
Network liveness
10%
score = min(100 − Σ wᵢ·pᵢ − pressure, caps)
QUARANTINED < 50
SUSPICIOUS
TRUSTED
back to TRUSTED only at 85; pressure ≤ 25, so forged traffic alone never quarantines; only clean authenticated evidence earns recovery time
Camera checks (signed by the vision service)
State
How it is measured
Effect
Occluded
dark, flat or blinded for 2 s
HIGH
Moved
shifted, or similarity < 0.7
HIGH
Frozen
the same frame repeated
HIGH
Degraded
low light or blur
MEDIUM
Too close
box > 35% of frame, not a distance
LOW
Source lost
no frames
MEDIUM
Tamper
HMAC report
+
Camera interference
signed, within 60 s
QUARANTINE
confirmed, score 30
Camera alone: a penalty, never quarantine. A camera report and a detection from the same signer count once.
Notes: Weights and caps: docs/architecture/trust-engine.md (design choices, not calibrated). Camera checks: ai/vision/health.py and ai/vision/proximity.py; tested on synthetic frames; on the live USB webcam a moving person produced no false camera-health report in 2 x 90 s. Covering, turning and freezing the real camera have not been staged. Proximity is image-space: no distance is measured.

## Slide 9
Q-Hack India 2026
Minimal Prototype
What we have actually built: running software, tested end to end
Gateway REAL
FastAPI + SQLite
Trust engine REAL
six factors, caps, states
PQC layer REAL
ML-KEM-768, ML-DSA-65
Vision service REAL
YOLO11n + camera checks
Quarantine REAL
enforced after authentication
Recovery REAL
orchestrator + deadlines
Digital twin REAL
expected vs reported
Evidence chain REAL
linked, signed, verified
Dashboard REAL
live view + presentation mode
Device agent SIMULATED
software, labelled
Attack simulator SIMULATED
synthetic, labelled
ESP32 firmware NOT YET
skeleton, not compiled
Self-healing recovery
Quarantine
Authorize
operator
Remediate
known-good config
Health checks
3 clean reports
Twin match
expected = reported
Verified
ramp begins
Recovered
score ≥ 50
Trusted
score ≥ 85
any failure → QUARANTINED: an authenticated fault, the 15-min verification deadline, the 2-h ramp deadline, revocation
Run it: python scripts/demo_full.py --webcam --pace 2 --hold
Notes: Everything marked REAL runs and is tested (785 Python and 40 JS tests). Device telemetry comes from a labelled software agent; attacks come from attack_simulation/ and are labelled; the ESP32 firmware has never been compiled. Repository: github.com/Zynx095/Q-shield.

## Slide 10
Q-Hack India 2026
Results / Validation
Validated on the real gateway with a real USB webcam; attacks are simulated and labelled
0
50
80
quarantine
suspicious
100
join
90
webcam
80
forged
72
replay
30
tamper
30
verified
80
recovered
85
trusted
Live run, 2026-10-02; recovery shown in announced time-lapse
Forged observation
REJECTED 401
Replayed observation
REJECTED 409
Tamper + signed visual evidence
QUARANTINED, score 30
Forged 'all clear' in quarantine
401
Verified recovery
TRUSTED 85; chain VERIFIED
785
Python tests passing
40
JavaScript tests passing
70
NIST ACVP vectors agree
10.0 ms
full PQC handshake (median)
~5 fps
live USB webcam, no false camera alarm in 2 × 90 s
Notes: Measured run of scripts/demo_full.py --webcam --pace 2 --hold: 100 -> 90 (real detections) -> 80 (forged) -> 72 SUSPICIOUS (replay) -> 30 QUARANTINED (tamper + signed visual) -> VERIFIED 30 -> RECOVERED 80 -> TRUSTED 85; evidence chain 26 entries, VERIFIED. Tests: python -m pytest (785 passed), node --test (40). ACVP: pqc/README.md. Detection accuracy has not been measured.

## Slide 11
Q-Hack India 2026
Roadmap
If selected for Round 2: from software prototype to a validated hardware deployment
1
Hardware bring-up
compile and flash the ESP32
match the 7 byte-exact protocol test vectors
reed switch, then BME280 and MPU6050
2
Staged validation
cover, turn, freeze and unplug the camera
open the enclosure
record false alarms and misses
3
Calibrate
set camera thresholds from recorded data
tune trust weights from incidents, not the demo
4
Harden
anchor the evidence head externally
key rotation, TLS by default
more than one gateway
5
Research
measure ML-KEM / ML-DSA on an ESP32-class device
a post-quantum device path if feasible
Hardware is an adapter step: same protocol, same gateway, same trust engine (docs/hardware/).
Notes: Plan from docs/hardware/hardware-architecture.md section 2 and docs/IMPLEMENTATION_STATUS.md 'What is left'. Nothing here has been done yet.

## Slide 12
Q-Hack India 2026
References and Sources
Standards, research, libraries and our repository
Standards
NIST FIPS 203, ML-KEM (2024) doi.org/10.6028/NIST.FIPS.203
NIST FIPS 204, ML-DSA (2024) doi.org/10.6028/NIST.FIPS.204
NIST SP 800-38D, GCM doi.org/10.6028/NIST.SP.800-38D
NIST FIPS 180-4, SHA-256 doi.org/10.6028/NIST.FIPS.180-4
RFC 5869 HKDF, RFC 2104 HMAC rfc-editor.org
NIST ACVP test vectors github.com/usnistgov/ACVP-Server
Research
P. W. Shor, Algorithms for quantum computation: discrete logarithms and factoring, FOCS 1994
L. K. Grover, A fast quantum mechanical algorithm for database search, STOC 1996
Libraries and tools
pqcrypto 1.0.0 (Apache-2.0): ML-KEM-768, ML-DSA-65
cryptography (PyCA): AES-256-GCM, HKDF
kyber-py, dilithium-py: test-only cross-checks
Ultralytics YOLO11n (AGPL-3.0), OpenCV, NumPy
FastAPI, Pydantic, SQLite
Our work
github.com/Zynx095/Q-shield
an original repository, not a fork; third-party libraries are dependencies under their licences
docs/: specifications, test results and limitations
Notes: All links are public. The repository contains the specifications (docs/architecture), the test and benchmark results (docs/results, docs/testing.md) and the limitations (README.md).